## Slide 1
Transport Layer OAM Protocol Considerations
Feng Yang (China Mobile)
IETF-125, March 2026

## Slide 2
Background
LEO satellite transport:
Non-congestive latency variation and loss
Time‑varying capacity
Frequent route/beam handover
HTTP/3 transfers test over Starlink[1]
High packet loss: 1.56% for downloads and 1.96% for uploads
High queuing delay: 95th RTT is 175ms when propagation delay is only 20ms
[1]MICHEL F, TREVISAN M, GIORDANO D, 2022. A first look at starlink performance. Proceedings of the 22nd ACM Internet Measurement Conference. ACM: 130-136.

## Slide 3
TCP variations: Hybla/CUBIC/BBR, etc.
  Bottleneck probe based on loss/delay/bandwidth
PEP / split connections:
  Splits TCP at satellite edges to hide long RTT
Explicit signal:
  link‑layer/physical info (fade, resource allocation, handover schedule) notification
Multi-Session:
  Uses several session concurrently to fill up bandwidth
Existing Work

## Slide 4
Problem Statement
In satellite networks, handovers between satellites and beams occur very frequently—Starlink, for instance, performs a handover approximately every 15 seconds.
Consequence is it will greatly impact transport protocol performance, and also waste of bandwidth.
If a handover causes a burst of packet losses, TCP would mistakenly interpret this as network congestion and revert from Congestion Avoidance back to Slow Start, then to ramp up again through Slow Start into Congestion Avoidance.
Transport protocol performance can be enhanced with kind of OAM capability:
Detect changes in delay, packet loss, etc;
  Rationale: cumulative/delayed ACK introduces more latency in the control loop.
Detect connectivity break/recovery time;
  Rationale: differentiate loss reason either by congestion or by handover.

## Slide 5
Transport Protocol OAM
Some options:
Per-session OAM:
  new message/flag/option for TCP/QUIC
  e.g. a new flag in TCP requesting immediate ACK
Multi-session shared OAM:
  IP layer connectivity detection, not impact by WRED/Congestion Control.
  e.g. BFD in echo or 2-way mode, transport layer can track connectivity state change as what BGP does.

## Slide 6
Use Cases
Per-session OAM: new flag in TCP requests immediate ACK in cwnd increasing window, which will be good for fast convergence of cwnd.
Multi-session shared OAM: using BFD to detect beam/satellite handover. TCP tracks state change of BFD.
  When BFD down, stop TX packets and freeze ssthresh/cwnd/rtt.
  When BFD up, recover the frozen variables.
Per-session OAM
Multi-session shared OAM
CWND
time
Slow start
Congestion Avoidance
ssthresh if congestion detected
ssthresh
ssthresh if handover detected

## Slide 7
Questions?